## Slide 1
Ana-Paula Bernardes EN-STI-RBS
ISCC
Tuesday 03rd of July 2012
Safety Issues

## Slide 2: Outline
Radioprotection
  REX post-accelerator radiation shielding
  Access
General Safety
  Oxygen deficiency hazard and access to the HIE-REX accelerator
  Pressure hazard
  Seismic hazard
Conclusion

## Slide 3: Outline
Radioprotection
  REX post-accelerator radiation shielding
  Access HIE-ISOLDE experimental area
General Safety
  Oxygen deficiency hazard and access to the HIE-REX accelerator
  Pressure hazard
  Seismic hazard
Conclusion

## Slide 4
Radioprotection
Shielding
Only X-rays drive the shielding:
Dose rate from X-Rays : several mSv/h at 1 meter from cryomodules
Dose rate from neutrons : Maximum of 200 μSv/h at 1 meter from the interaction point
Acknowledgement S.Maridor

## Slide 5
Radioprotection
Shielding studies: (Acknowledgement J.Vollaire and S.Giron):
Measurements campaign by DGS-RP in agreement with cryomodule test schedule (conditioning and during nominal conditions)
Shielding sizing based on LNL data (7 mSv/h inner side of shielding – distance of 3 meters) as envelop scenario for the shielding in order to go ahead with tunnel integration
Started by DGS/RP

## Slide 6
< 1μSv/h at 1m
< 4μSv/h at 1m
< 200μSv/h at 1m
Exceptional procedure used for example during commissionning
 Specific safety measures will be put in place and beam permit will be requested
Normal operation - Data used for defining access to the experimental area
Strategy for experimental Hall for HIE-ISOLDE Collaboration J.Vollaire, F.Wenander, D.Voulot
Acknowledgement D.Voulot – Data extract from EDMS 1224228 “Specification of the sources of radiation and maximum beam intensities and energies of the HIE-ISOLDE Linac”
Radioprotection

## Slide 7
Radioprotection
No Access Control for the experimental
Access system with key (interlocked with RF power)

## Slide 8
Radioprotection
Area classification change due to presence of contamination
Picture from V.Barozier
Supervised area
Existing Building 170
In near future on request of RP
(D < 6mSv/year)
Controlled area
Supervised area  Controlled area:
No more VCT (Short term visitor)
Medical certificate mandatory to get the dosimeter
No visitor allowed (only technical visits)

## Slide 9: Outline
Radioprotection
  REX post-accelerator radiation shielding
  Access HIE-ISOLDE experimental area
General Safety
  Oxygen deficiency hazard and access to the HIE-REX accelerator
  Pressure hazard
  Seismic hazard
Conclusion

## Slide 10
Pressure Hazard
Pressure Equipment shall be designed following CERN Safety rules:
General Safety Instruction on standard pressure equipment (GSI-M2) EDMS 875610  European directive 97/23/EC
In complement EN 13458 standard on “Cryogenics vessels – Static vacuum insulated vessels”
“pressure equipment” means vessels, piping, safety and pressure accessories, not exposed to open flame, and subject to a maximum allowable pressure greater than 0.5 bar
Vacuum insulated vessel PS<0.5 bar
Not considered as pressure vessel from European directive definition – No EC marking is requested
Acknowledgement Y.Leclercq

## Slide 11
Pressure Hazard
Pressure Equipment shall be designed following CERN Safety rules:
General Safety Instruction on standard pressure equipment (GSI-M2) EDMS 875610  European directive 97/23/EC
In complement EN 13458 standard on “Cryogenics vessels – Static vacuum insulated vessels”
For the LHe tank and the Solenoid:
PS  4 bars
Considered as pressure vessel from European directive definition – EC marking is requested
Pressure and leak tests will be requested
Category II
Cavities  Category II but no CE marking will be requested
Acknowledgement Y.Leclercq

## Slide 12
Cryogenic Hazard
In addition cryogenic installation shall comply with CERN rule :
IS47 “the use of cryogenics fluids” EDMS 335812
“The liquid container shall be protected against overpressure by a minimum of two
relief devices in parallel, preferably of different types…”
Acknowledgement N.Delruelle
2 safety valves for all cryogenics equipment containing LHe

## Slide 13
Cryogenic Hazard
Cryogenic Released Scenarios needed for safety devices sizing (Acknowledgement N.Delruelle)
Total loss of cryomodule insulation vacuum  2 safety valves will release He outside of HIE-ISOLDE tunnel
No release inside tunnel  No asphyxia hazard for people
Collaboration N.Delruelle et C.Parente

## Slide 14
Cryogenic Hazard
Cryogenic Released Scenarios needed for safety devices sizing (Acknowledgement Y.Leclercq)
Total rupture of one connection between LHe tank and cavity  1 safety valve (Final sizing to be done)
Two options open:
Collecting output from safety valves and routing to tunnel openings
No collecting but specific procedure to access the tunnel under discussion
Cryomodule insulation vacuum safety valve
Collaboration Y.Leclecrq et C.Parente

## Slide 15
Seismic
Infrastructure and sensitive equipment shall be designed following CERN Sismic Safety rules:
The French territory is divided in five seismic zones from very low seismicity (seismic zone 1) to strong seismicity (seismic zone 5) – EDMS 1158454
CERN is classified as seismic zone 3

## Slide 16
Seismic
All building including tunnel are concerned as well as some equipment:
Cryoplant
Cryomodules
Jacks to comply with seismic rules
Cryomodule/jack connection to comply with seismic rules
Acknowledgement Y.Leclercq

## Slide 17
Conclusion
Radioprotection
Shielding
  X-Ray measurements on going
  Use of envelope case from Legnaro for shielding specification
No Access Control for the experimental Hall expected – to be confirmed by DGS/RP
General Safety
  Option for cryogenic safety may allowed access when cavities are cold  to be confirmed by the safety unit DGS/SEE
  Specific procedure before access may be needed

## Slide 18: Acknowledgement
Thank you very much for your attention
EN/HDO : Y.KADI,
BE/OP : E.SIESLING, D.VOULOT
BE-RF : M.FRASER
GS/SE : D.PARCHET, E.PEREZ-DUENAS
EN/CV : P.PEPINSTER, A.POLATO
TE/ABT : B.GODDARD
TE/CRG : N.DELRUELLE
TE/MSC : Y.LECLERCQ, D.SMEKENS, JP.TOCK, L.WILLIAMS
EN/STI : R.CATHERALL, Y.ROMANETS
EN/MEF : S.MARIDOR
EN/MME : V.BAROZIER
GS/DI : C.BEDEL
GS/ASE : D.CHAPUIS, D.RAFFOURT, F.SCHMITT
DGS/RP : A.DORSIVAL, J.VOLLAIRE
DGS/SEE : J. BATISTA LOPEZ, C.PARENTE, D.PHAN
CEA : V.BLIDEANU, A.VAN LAUWE

## Slide 19: Radiation levels (Neugam code)
30 rem/h = 300 mSv/h
2.5 pmA of Kr = 300 mSv/h
0.5 pnA expected = 60 mSv/h
Source : ATLAS (ANL) Safety Assessment Document
Reserved slides

## Slide 20
Reserved slides
Neutron dose rate at 1 m and at 90° from the interaction point of ions bombarding a
medium mass target (Fe, Ni or Cu) from Moritz, L. TRIUMF ISAC2 safety report. s.l. : TRIUMF, 2006.