## Slide 1: HIE-ISOLDE The technical options
Yacine Kadi, Mats Lindroos and Matteo Pasini, the ISOLDE technical team and the ISOLDE collaboration

## Slide 2: HIE-ISOLDE: Next step with three objectives
ENERGY: REX energy upgrade and increase of current capacity (Matteo Pasini)
  Energy upgrade in 3 stages: 8 MeV and 10 MeV/u and lower energy capacity
QUALITY: ISOLDE radioactive ion beam quality – more than half already financed through the ISOLDE collaboration
  Smaller longitudinal and transverse emittance
    Done
  RILIS upgrade and LARIS construction
    Done
  Charge breeder upgrade
  Better mass resolution
  Continued target and ion source developments
    On-going and absolutely essential!
INTENSITY: ISOLDE proton driver beam intensity upgrade - strongly linked to PS Booster improvements including linac4 (INTENSITY WP, Richard Catherall)
  Faster cycling of the booster
  New target stations for ISOLDE
  New target design
  New target handling system

## Slide 3: HIE-ISOLDE project
HIE-ISOLDE 1
  Energy upgrade up to 8-10 MeV/u with a superconducting linac, beam quality improvements and the design study of the intensity upgrade
    R&D activity for LINAC funded
HIE-ISOLDE 2
  Intensity upgrade for 30 kW on target
    Linac 4 beam via PSB and Light SPL beam to ISOLDE
  Super-HRS

## Slide 4: Existing REX-ISOLDE linac – a world leading RIB facility

## Slide 5: HIE-ISOLDE LINAC - layout
3 stages installation
1.2 MeV/u
3
MeV/u
5.5 MeV/u
M. Pasini EURISOL Town Meeting Pisa, 30.03-01.04 2009
10 MeV/u
8
MeV/u

## Slide 6: HIE-ISOLDE SC-linac
SC-linac between 1.2 and 10 MeV/u
Energy fully variable; energy spread and bunch length are tunable. Average synchronous phase fs= -20 deg
2.5<A/q<4.5 limited by the room temperature cavity
16.02 m length (without matching section)
No ad-hoc longitudinal matching section (incorporated in the lattice)

## Slide 7: Final Beam Energies
M. Pasini EURISOL Town Meeting Pisa, 30.03-01.04 2009
N.B! With ECR technology:
A/q=6 7.9 MeV/u
A/q=9 5.4 MeV/u

## Slide 8: Cavity prototype

## Slide 9: Cryomodule design
This concept foresees the possibility to align the solenoid when cold from the outside (beam alignment)
Common vacuum concept to minimize the inter-cryomodule distance
Each cryomodule can be isolated and taken out in case of failure.

## Slide 10: HIE-ISOLDE SC linac

## Slide 11: Buildings and infrastructures
M. Pasini EURISOL Town Meeting Pisa, 30.03-01.04 2009

## Slide 12: DOE proposal - Comparison EBIS/ECR/1+
 | Proposed High-Intensity EBIT | MSU EBIT | TITAN EBIT | BNL test EBIS | REX-EBIS
Electron beam energy (keV) | < 60 | < 30 | < 60 | <30 | < 6
Electron beam current (A) | < 10 | < 5 | <5 | <20 | < 0.5
Central current density (A/cm2) | <105 | <104 | <104 | <600 | <200
Magnet design | Helmholtz Coil + Solenoid | Helmholtz Coil + Solenoid | Helmholtz Coil | Solenoid | Solenoid
Maximum magnetic field (T) | 9 | 6 | 6 | 5 | 2
Trap length (m) | 1 m | 0.5 m | 0.1 m | 0.7 m | 0.8 m
O. Kester et al.

## Slide 13: RFQ cooler “ISCOOL” - DONE EPSCR grant (Manchester, Birmingham)
Emittance meter
RFQ cooler
Alkali ion source
Continuous mode
~5p·mm·mrad 90% emittance
~30p·mm·mrad 90% emittance as input
Ion | transmission
Li+ | 17%
Na+ | 27%
K+ | 60%
Cs+ | 70%

## Slide 14: The Resonance Ionization Laser Ion Source
4 types of ionization scheme:
RILIS beams of 28 elements are available so far:
2-step: (1 resonance)
(2 resonance)
3-step: (2 resonance)
(3 resonance)

## Slide 15: New Nd:YAG lasers at ISOLDE RILIS - DONE
Two dye lasers were applied at 1st step of excitation - x 2
More power could be delivered to HRS target at the 2nd step of excitation
Better power stability
Diode Pumped Solid State Nd:YAG Lasers as replacement of Copper Vapor Lasers:
Green Beams
45 W @ 511 nm
Yellow Beams
35 W @ 578 nm
CVL
Green Beams
90 - 100 W @ 532 nm
UV Beam
18 W @ 355 nm
IR Beam
35 W @ 1064 nm
SSL
15 ns @ 11 kHz 8 ns @ 10 kHz
46%
54%
46%
Improvement of Ga ionization efficiency by SSL :
CVL scheme
SSL scheme
Knut and Alice Wallenberg foundation grant

## Slide 16
LARIS results – A new RILIS scheme for Manganese - DONE
- Replacement of current scheme which uses the CVL green beam.
Fortuitous
Auto-ionizing transition
at CVL wavelength
Outcome of RIS study of Mn at LARIS:
Many new auto-ionizing states found
Various promising Nd:YAG based schemes tested and ready for efficiency measurement at RILIS
AIS search at LARIS
Knut and Alice Wallenberg foundation grant

## Slide 17
Road map of RILIS upgrade
Installation of solid state lasers for dye laser pumping. Keeping CVL lasers at RILIS as backup until reliable SSL performance is reached.
Upgrade of dye lasers: purchasing and installation of commercial dye lasers
Installation of solid-state tunable lasers with own pump laser in addition to the dye laser system
Duo-RILIS: two laser systems available for operation with a possibility of quick switch from one element to another
2008
2009
2010
2011
Knut and Alice Wallenberg foundation grant

## Slide 18
ISOLDE target area - The 3D Laser Scan
Reference Points
Cloud of point in the CERN coordinate system
J. Sarret, L. Bruno

## Slide 19: Manipulator concept design
6-DOF Manipulator mounted on ceiling monorails
Equipped with tool changer for mounting different tools
Recoverable by decoupling (remotely) rail gear drive
High lifting capacity (FFE)
Target & electrode accurate / sensitive operations

## Slide 20: Overall layout of the new injectors (1/2)
SPS
PS2
SPL
Linac4
PS
ISOLDE

## Slide 21: Analysis
SPL block diagram
Main impact of faster cycling rate: klystron modulators (SPL + Linac4)
Limited Paverage + technology limited cycling rate (~ 15 Hz)
Paverage µ Modulator pulse length x Rep. rate
Paverage µ (Modulator rise + Cavity fill + Beam pulse) x Rep. rate
Other consequences of faster cycling rate:
  Magnets power supplies
  Beam instrumentation
  Controls…
Linac4
b=0.65
b=1
b=1
b=1
160 MeV
732 MeV
(560 MeV)
1.4 GeV
(1 GeV)
2.5 GeV
4-5 GeV
Extraction to ISOLDE
µ Eacc2
200 ms

## Slide 22: Minimum cost options
Beam energy (GeV) | Max. pulse duration (ms) | Max. current during pulse (mA) | Cycling rate* (Hz) | Max. protons /pulse (x1013) | Max. beam power (kW)
1.4 | 0.9 | 20 | 1.25 (3 out of 4 pulses) | 11 | 31
1 | 0.35 | 28 | 2.92 (7 out of 8 pulses) | 6.1 | 29
* Basic period : 600 ms – PS2 cycling time: 2.4 s
Baseline solution
Need for wide range high power RF phase shifters… => Cost!
LP-SPL type modulators (Pnominal º 0.35 % duty cycle)

## Slide 23: Summary
Planning for a staged implementation project
HIE-ISOLDE 1
  HIE LINAC R&D within the EUCARD I3 and with Belgium grant is making good progress
  Test of the first cavity for the SC linac are expected in June/July at TRIUMF in Vancouver
  On-going beam quality development e.g. RFQ cooler and RILIS
  Construction of linac and design study of new target area
HIE-ISOLDE 2
  Construction of new target area and Super-HRS
  Linac 4 (10 kW) and LP-SPL (30 kW)
M. Pasini EURISOL Town Meeting Pisa, 30.03-01.04 2009