## Slide 1
  Introduction:
Strong physics case for decay studies at ISOLDE using an efficient germanium array surrounding an implantation/decay station
  Approved experiments:
    IS456: Study of polonium isotopes ground state properties by simultaneous atomic- and ...
    IS474: Fast-timing studies of nuclei below 68Ni populated in the beta-decay of Mn isotopes
    IS476: Studies of beta-delayed two-proton emission: The cases of 31Ar and 35Ca
    IS507: Study of the beta-decay of 20Mg
    IS525: Study of multi-neutron emission in the beta-decay of 11Li
    IS534: Beta-delayed fission, laser spectroscopy and shape-coexistence studies with radioactive...
    IS545: Experimental investigation of decay properties of neutron deficient 116-118Ba isotopes .....
  Beam development creates new opportunities for (pioneering) decay studies
Current situation:
  removable detection systems (at LA1 or GLM)
  limited germanium detection efficiency
 need for a fixed set-up with an efficient germanium array and ancillary detectors
Original idea: use of Miniball detectors and/or Miniball position (Miniball workshop March 5-6, 2012 Koln)
  Moving Miniball clusters is cumbersome and risky
  Not compatible with Coulex and transfer reaction set-up
Fixed Decay Station at ISOLDE

## Slide 2
Fixed Decay Station at ISOLDE
  Proposal:
Fixed decay station position at ISOLDE
  LA1, former Mistrall or other beam port
Miniball type or clover type germanium detectors positioned around a decay station:
source to detector distance ~ 5-10 cm: flexible holding structure
  tape system with plastic scintillator detectors for beta detection: b-decay studies
  windmill or equivalent system hosting carbon foils and silicon detectors: a-decay, b-delayed fission, b-delayed charge particle studies
  neutron detectors: b-delayed neutron studies
  fast timing detectors
  anti-Compton shields
  Needs:
    good and reproducible ISOLDE beam transmission
    proper beam diagnostics and definition
    DAQ: compatible with ISOLDE DAQ developments
    space for TOF neutron detectors and for flexible mounting of germanium detectors and shielding.

## Slide 3
  Collaboration/interest:
Positive response:
  Spain (Madrid, Valencia), UK (Paisley, York, Liverpool), Germany (Koln, Darmstadt, Munchen), Denmark (Aarhus), Sweden (Lund), France (Bordeaux), Finland (Jyvaskyla), Switzerland (ISOLDE) and Belgium (Leuven)
ISOLDE Decay Station Workshop: October 3, 2012 in CERN
  Physics case
  Hardware, detectors and electronics
  Resources: what exists in the collaboration - permanent physicist at ISOLDE
  Task list/timeline
  Collaboration
Fixed Decay Station at ISOLDE