## Slide 1: ISOLDE Technical Report for the ISCC
Richard Catherall EN-STI
CERN, 3rd July 2012

## Slide 2: Agenda
Operations
  Targets (T. Stora)
  REX (D. Voulot)
  RILIS (V. Fedosseev)
  Infrastructure
Safety
Target Area Upgrade
  Design Study
  Robot replacement
  Hot Cell
  PAD/MAD
  Medicis
  Handling & transport
  Proposition

## Slide 3
Molten salt target for b-beams 18Ne beams (n emitter)
T.M. Mendonça1, B. Crepieux1, M. Owen1, E. Barbero1, S. Marzari1, S. Cimino1, R. Hodak2, M. Allibert3, V. Ghetta3, D. Heuer3, E. Noah4, T. Stora1
TISD team + MM-MME & TE-VSC contributions
1 EN-STI-RBS, 2 Comenius University Bratislava, 3 LPSC Grenoble, 4 DPN, Univ. Genève
INTC – IS 509
18Ne ISOL beam @ ISOLDE
from static salt target:
Concept
Salt condensation
Yield,
D [m2/s]
6mA
160MeV
2.1 L/s
7.5x24x15cm
40x15x15cm
Transfer line
to ion source
CERN-2010-03 p110
23Na(p, X)18Ne, 19F(p,2n)18Ne
Technical achievements:
Haynes 242 Alloy
(special machining,
corrosion resistant)
NaFLiF eutect. synthesis
Salt vapor condensation
(phase diagram, hydrolysis,
Fluka, ANSYS,
Ta+Alumina oven
Thermocouples)
Online with Protons !
800kW
NaF:LiF (39-61% eutectic
melt 650C)

## Slide 4
- Article is chosen as the EPL editor “highlight” (to be published in a next issue).
- First experimental demonstration of high intensity beam of 6He
on BeO target by (n,a) reaction with spallation neutrons
New theoretical fit of isotope release based on diffusion and evaporation time constants from ISOLDE targets
Molten salt target:
Results at ISOLDE already anticipated in CERN’s activity report

## Slide 5: Pb/Bi loop online tests in 2015 for EURISOL
Institutes | Role in the collaboration | Person(s)
LENAC/SPhN/IRFU, CEA, Saclay | Safety file and licensing | V. Blideanu, A. Marchix
PSI, Villingen | Instrumentation | D. Schumann
IPUL, Salaspils | Offline Pb/Bi loop tests | K. Kravalis, E. Platacis
SINP, Kolkata | Radiochemistry | S. Lahiri
CERN, Geneva | Coordination, Design, ISOLDE interface, online tests | T. Stora, A. P. Bernardes, J. Vollaire, M. Delonca, C. Maglioni
SCK-CEN, Mol | CFD simulations, selection of components | P. Schuurmans, L. Popescu, M. Schyns
Kick-off 10th May
4 years project
Endorsed by CERN A&T sector
Budget 450 kCHF + in-kind contrib.

## Slide 6
ActiLab (JRA in FP7-ENSAR) & Actinet
2mm
Identification of open porosity and grain size at the mm/sub-mm level in ISOLDE UCx
Before irradiation (contrary to previous publications in the field)
A. Gottberg, J.P. Ramos, C. Degueldre, C. Borca, D. Grolimund, I. Günther-Leopold, A. Andrighetto, C. Lau, P. Delahaye and T. Stora
FIB and Swiss Light Source @PSI

## Slide 7
New air conditioning for RILIS
Air temperature in RILIS laser room is higher but more stable.
Air humidity is low and constant
Drift of laser beams is reduced
Installed during the winter shutdown
Laser cooling chiller moved to the roof:

## Slide 8
Piezo actuators for fast beam displacement
Currently capable of stabilizing up to two visible or IR beams
Laser beam stabilization
Stabilization of high and low frequency beam fluctuations
Commercial system adapted to RILIS conditions

## Slide 9
RILIS status monitoring
Essential RILIS parameters are published to a Labview DSM.
All values are accessible from the CERN technical network
RILIS monitor display is published to a website for remote monitoring
Power
Wavelength
Proton current
Reference beam
images
https://riliselements.web.cern.ch/riliselements/LASERS/

## Slide 10
New RILIS beam: Calcium
Strong transitions to Auto-ionization states are found by scanning the wavelength of 3rd step dye laser:
The ionization scheme of Ca is developed applying combination of Ti:Sapphire and dye lasers
Ti:Sa laser + frequency doubling
dye laser
dye laser
Laser / Surface > 100
Used for IS529, IS532

## Slide 11: REX campaign 2012
IS524 123Cd
(2) IS478 72Kr
Finally successful!
(3) IS496 140,142Sm
...
* Already two successful runs, one ongoing
* 10 runs schedule until September (+ a few more until November)
Many beamtime request for HIE-ISOLDE MDs
-> transverse emittance measurements
-> HIE diagnostics box commissioning
-> Si-det test for TOF measurement
-> PIN-diode detector for EBIS slow extraction signal
-> RP measurement of X-ray background in the hall
->...
Emittance meter behind the linac
HIE diag. box on L20 (BE/BI)

## Slide 12: Improvement of RFQ section vacuum
New turbo installed on RFQ section
Replacement of vacuum window for MCP system in DB2
Now all the section is < 5e-7 mb
Presently running 142Sm34+ no sign of transmission loss

## Slide 13: Infrastructure
Migration of GM classes to the CERN standard FESA classes for most of the equipment at ISOLDE.
  Magnet controls to follow suit.
Tests on automatic beam transport optimization successful
Application interlock on beam intercepting devices in path of laser green light
Fencing of ISOLDE hill (to be refined)

## Slide 14: ISCOOL RF amplifier
New RF amplifier has been tested offline
Hardware installed in RFQCB cage, ready for commissioning (waiting for cabling)
Control system hardware to be installed in July (VME crate + fiber optics ethernet connection)
Aiming for operational test and validation in the second half of the runs
(Full control system with OASIS monitoring signals and console application to be deployed later)

## Slide 15: Non-InCA architecture
...

## Slide 16: Injector Controls Architecture
...

## Slide 17
Safety course specific to ISOLDE primary area on line on SIR 
Objective: Be prepared for the LS1
(Link with access data base planned for December 2012)
 CEA/IRFU/LENAC and CERN Safety collaboration started to perform various safety studies on target prototype
  ALARA addressed by EN-STI-RBS in 2012 ISOLDE
    5 ALARA III
    9 ALARA II

## Slide 18: Agenda
Operations
  Targets (T. Stora)
  REX (D. Voulot)
  RILIS (V. Fedosseev)
  Infrastructure
Safety
Target Area Upgrade
  Design Study
  Robot replacement
  Hot Cell
  PAD/MAD
  Medicis
  Handling & transport
  Proposition

## Slide 19: HIE-DS design study
Activated air release/ventilation
  WP of HIE Design study (by Andrea Polato)
  Creation of a SAS between target area and the class A laboratory
  Target and beam dump cooling
  Reduction of contamination risks from target area to class A laboratory
  Best efficiency of the ventilation
SAS ?

## Slide 20: HIE-DS design study
Additional shielding
  WP of HIE Design study (L. Morejon)
  Creation of 2 removable shielded close to targets
  Reduction of air activation into the target area
  Fluka Simulation under study

## Slide 21: Robot Upgrade

## Slide 22: Robot Upgrade
Test stand almost complete
Test of long cables done
Integration on-going
  Issue in front of GPS faraday cage
New gripper design with quick release
Interlocks, redundancy, functional requirements …etc

## Slide 23: Hot Cell
Functional specs completed
Technical specs under completion
Market survey has been launched
Aiming for the December 2012 Finance Committee
Oxidation process to be finalized this year
New buffer zone in IS5 complete

## Slide 24: PAD-MAD Access
CHECK POINT RP
PAD
CLEFS
MMAD
EDMS no.1145495
Installation planned for the end of 2013
Version with new target storage being investigated
Robot barrier will be integrated
MAD can be removed for Front End passage
No PAD/MAD in the hall for secondary zones
- physically impossible
An alternative solution is under investigation

## Slide 25: MEDICIS
New RABIT for MEDICIS
  Project under inquiry (S.Marzari)
  Informal market survey done
  Functional specification done
  Possibility to irradiate samples just ahead the beam dump
  Pneumatic fast transportation from irradiation station to the hot cell

## Slide 26: MEDICIS
MEDICIS principle
KT Fund
Freely available

## Slide 27: Target life cycle and Handling
Move by lots of 6 hot target/pallet to ISR
Return by lots of 6 decayed targets/pallet to Isolde for dismantling in the hot cell
Move waste containers into the truck for Paul Schaerer Institut (PSI)
Deliver the new target to the exchange point for the robots by hand
Pallet Handling with
1 remote controlled
Vehicle (existing)
To PSI (1/y)
New hot
Cell (2013)
New
Target
To ISR (~3 transports/year 3x10 = 30 targets/year)
Back from ISR (~4/y)
19 m2 area for container storage and for targets back from ISR waiting for hot cell dismantling (too small ?)
By Robots

## Slide 28: Overview
Strong interactions between projects
New Hot cell
2 New Robots
New Cameras
PAD-MAD
New ventilation
and cooling
Additional
shielding
New storages
Remote handling vehicle
New RABIT
MEDICIS lab
Targets-frontend
upgrade
Approved projects 2013
HIE-Design study
Handling optimisation
MEDICIS

## Slide 29: Integration
Proposed Layout :
In green: Approved projects
new robots,
cameras,
PAD-MAD,
hot cell
In orange: HIE-DS
new ventilation and cooling,
additional shielding,
targets and frontend upgrade
In blue: new storage and MEDICIS

## Slide 30
Handling optimisation
New remote handling vehicle
  Project under inquiry (by Keith Kersaw & Stefano Marzari)
  Informal market survey and potential suppliers visit done
  Reduction of risks for hot target transportation
  Add new functionalities and flexibilities like:
    Hot target autopsy
    Increase re-use of old targets for Isolde facility
    Recovery/backup of Kuka Robots
    Camera inspections
  Simplifications in ALARA committees
Possible design examples

## Slide 31: Thank you for your attention
Acknowledgements
  A-P. Bernardes
  S. Marzari
  A. Stadler
  T. Stora
  GS-ASE, BE-OP
  D. Voulot
  V. Fedosseev
  L. Hernandez, V. Vlachoudis
  J-L. Grenard, B. Feral, K. Kershaw
  A. Polato
  G. Kruk