## Slide 1: ISOLDE Technical Report for the ISCC
Richard Catherall EN-STI
CERN, 31st January 2012

## Slide 2: Agenda
Targets
REX
RILIS
Shutdown work 2011/2012
  Water cooling
  Access
  INCA
  Timing
Safety
News from EN

## Slide 3: Targets
A third target nanomaterial (SiC, Y2O3, CaO) for ISOLDE 35Ar from CaO469-VD7 for Proprietary CERN technology J. Nucl. Mat. 416, 99 (2011)
Yields on 31,32Ar measured by ISOLDE experiment IS476 – H. Fynbo and B. Blank.
Turrion, M.; Urszula, H.-I. ISOLDE Yield Database. https://oraweb.cern.ch/pls/isolde/query_tgt (accessed December 1st, 2011)
TRIUMF. ISAC Yield Measurement. http://www.triumf.info/facility/research_fac/yield.php (accessed December 5th, 2011)
GANIL. SPIRAL Beams. http://pro.ganil-spiral2.eu/users-guide/accelerators/spiral-beams (accessed December 5th, 2011)
Ions per second | 31Ar (15.1ms) | 32Ar (98ms) | 33Ar (174.1ms) | 34Ar (844ms) | 35Ar (1.78s)
ISOLDE | 6.3E+01 | 3.6E+03 | 2.0E+05 | 2.6E+06 | 3.0E+08
TRIUMF | - | - | 7.0E+02 | 2.9E+04 | 6.5E+06
T. Stora

## Slide 4
1. Addition of FC readout channels
Avoid having to move cables between XL65 and XL20 line
when reading out Miniball and beta-NMR FCs
- XEBS.FC20: new FC installed at the same location as EBIS.BO10
- XL65.FC100: new PAM for the Miniball FC
- XL20. FC100: new PAM for the beta-NMR FC
2. REX controls upgrade
Discussion about an upgrade of a number REX controls items have started.
Four work packages identified.
WP1: PLC/RS422 Controlled Power-supplies
WP2: REX magnetic field regulation
WP3: REX Linac RF Controls
    WP4: REX EBIS pulsed power-converters
Work to be carried out between now and end of LS1
REX improvements
3. Increased performance of the new REXTRAP RF excitation (e.g. reduced loading time)
F. Wenander

## Slide 5: REX consolidation and improvements
Linac cooling water
  Several trips during 2011
  Flow can be reduced on the BTY line magnets -> Install flow regulators (gain ~7 m3/h)
Vacuum upgrade in RFQ section (high losses with highly charged ions)
  New Hi-pace pump installed in front of RFQ
  Renovation of DB2 (this shutdown)
Enable 2 ms RF pulse length on all amplifiers for slow extraction (this shutdown)
  Max rep rate: 50 Hz without 9-gap / 15-20 Hz with 9-gap
  Need reduced power for the 9-gap -> lower max energy
D. Voulot

## Slide 6: 9-gap amplifier upgrade
Upgrade of 9-gap amplifier to ensure stable operation during the 2014-2018 period
Replace final stage tube, 130 kW, 2 ms pulse length
Estimated cost 300 k€
Commissioning early 2014
D. Voulot, H. Broere

## Slide 7
New IrCe cathode
Modified
Wehnelt
electrode
Courtesy of T. Berg
TwinEBIS testbench
Project 2. Detect low-intensity stable beam contamination using an MCP
* Install the equipment (2 dedicated MCPs and vacuum chamber)
* Set up electronics for particle counting of low-energetic (30-60 keV) ions
* Evaluate the setup, i.e. test efficiencies, counting rates etc
* Estimated time 3 months
  Contact persons: F. Wenander, M. Kowalska and B. Marsh
Call for support by external students
Project 1. Setup the TwinEBIS testbench
a. Finalize design and installation of mechanical parts, 6 months
b. Re-commission superconducting solenoid
c. Produce a control system for power supplies, current readouts,
vacuum control system, interlocks. Labview experience, 6-9 months
d. Commission the source, test alternative cathode and gun types,
increase electron beam current and energy. Electron beam
simulations. >12 months
Experienced student(s)
Contact person: F. Wenander

## Slide 8
Beam | Sm | Ga | Mg | At | Pb | Dy | Nd | Pr | Ag | Tl | Cd | Mn | Ni | Yb | Zn
Planned | 80 | 104 | 256 | 160 | 184 | 64 | 136 | - | 112 | 208 | 288 | 120 | 272 | - | 376
Real | 89 | 101 | 146 | 269 | 221 | 35 | 110 | 4 | 92 | 231 | 242 | 390 | 348 | 73 | 407
RILIS operation
2756 h – Total
2527 h – On-line
> 50 % of the
Total running time of ISOLDE facility
Laser ON time
in 2011:
Ion beams of 15 elements were produced
V. Fedosseev, B. Marsh

## Slide 9: ISOLDE RILIS development
New ion beam - Astatine
May 2011 (b, c) :
6 ionization schemes were compared
up to 150 pA of 205At was obtained
August 2011(d) :
A series of Rydberg states observed
At ionization potential measured precisely
Dye laser scan,
At-205 ion current measured with a Faraday cap

## Slide 10: Shutdown Work
Beam instrumentation
  Exchange of double scanner unit in HRS separator zone
  Displacement of PAM’s externally to HRS separator zone.
  Migration of PLC software for PAM’s Grids and FNBS to IEPLC standard
General maintenance
  Electricity, ventilation, robots, water, vacuum, laser window exchange….etc
Controls applications
  Upgrade of various applications
  TIMBER traceability on-going
Front End maintenance
  Faraday cage pistons to be replaced with “nuclearized” pistons & new cabling
  New HT cable to be pulled through HT transfer tube
Target ramping cards
  Installation of controlled current reduction cards (ramping cards) for GPS & HRS target & EBIS cathode power supplies

## Slide 11: Water cooling system
Modifications of the existing target cooling system
  Refilling of reservoir with “clean” demineralized water from another circuit.
    Previous filled from target station closed circuit
  Diversion of water drainage
  Modification of controls to implement a delay before switching to reservoir
  Independent pressure regulation of GPS and HRS water circuits
Tests on cavity cooling using 27C water cooling
  New HIE-ISOLDE specs for cooling tower.
  May need a water cooling sub-station?

## Slide 12: Access to ISOLDE
Following report by RP on the evaluation of the shielding at ISOLDE
  EDMS 1142606
Fencing to be put up before start up.
Turnstile will be moved to new sas in
E. Siesling

## Slide 13
INjector Control Architecture @
based protocol
System INCA
Application server
Control room workstation
Working set
Knob
Specific applications
CMW (middleware)
FEC (Front End Computer)
FESA server
Real Time tasks
3-tier Architecture
Advantages:
Better performance thanks to centralised computing
Settings history logged in DB
Better scalability
Better security
INCA deployments status:
PSB & LINAC 2
PS
LEIR & LINAC 3
SPS
ISOLDE
2012
Why at Isolde?
Control system uniformity within the accelerators complex
More flexibility and customization capabilities
E.Piselli (BE-OP-PSB)

## Slide 14: Timing Signals Renovation
T. Giles, P. Fernier

## Slide 15
General Safety
ISOLDE Primary area inspection by the French and Swiss authorities  Few minor remarks
Web based safety course will be requested to get the access rights of the primary area
A-P Bernardes

## Slide 16: Safety
Supervised area
Existing Building 170
Date to be discuss with RP
(D < 6mSv/year)
Controlled area
Supervised area  Controlled area:
No more VCT (Short term visitor)
Medical certificate mandatory to get the dosimeter
No visitor allowed (only technical visits)
A-P Bernardes

## Slide 17
2 new Kuka linear Robots
In Isolde Target Area
(2013)
Target life cycle and Handling
Deliver the new target to the exchange point for the Kuka robots
Remove hot target and place on the shelf (during shut down)
Move the 3 years decayed target from shelf to hot cell
Move waste containers (with “standard” trans-pallet)
Handling with
1 remote controlled
vehicle
To PSI
New hot
Cell (2013)
New
Target
S. Marzari

## Slide 18
HRS Shielding improvement
New storage
~200m2 for nuclear medicine
~5000 m3 earth removal
S. Marzari, T. Stora

## Slide 19: Civil engineering overview
Building 115
Class C lab
Building 507
Light building
TSR extension
Building 199
cold box
Building 198
Compressor room
Medical Isotope
Facility
Target area extension

## Slide 20: Thank You
To the ISOLDE team and all the supporting groups
…and for your attention